## Slide 1
Welcome to my presentation

## Slide 2
TECHNOLOGY UNIVERSITY(KALAY)
DEPARTMENT OF ELECTRONIC
ENGINEERING
Supervisor – Daw Cho Thet Nwe
Presented by
Mg Aung Ye Htet ( VI EC- 47 )
Defense 6.10.2018
DESIGN AND IMPLEMENTATION OF
ROBOTIC ARM
(Android Software Implementation)

## Slide 3: Outline of Presentation
Abstract
Aim and Objectives
Introduction
Overall System Block Diagram
Application Areas
Android Software
Implementation Program
Expected Outcomes
Conclusion
Arduino Software Implementation
Circuit Implementation
Hardware Implementation

## Slide 4: Abstract
An articulated robotic arm is designed and implemented to pick up the weight of 300g by controlling android phone.
Arduino microcontroller is the main control function of the system.
Bluetooth module supports robotic arm as a wireless interface between the robotic arm and the android phone.
There are five joints in robotic arm so that it support five degree of freedom to perfectly work of gripping.

## Slide 5: Aim and Objectives
To design and implement of Robotic Arm
To evaluate the mathematical coordinates

## Slide 6
Introduction
A robot consisting of parts linked together in the same way as those of a human arm, mounted on a stand.
The most common manufacturing robot is the robot arm which is usually made up of several metal segments.

## Slide 7: Types of Robotic Arm
Cartesian Robotic Arm
Cylindrical Robotic Arm
Polar Robotic Arm
SCARA Robotic Arm
Articulated Robotic Arm

## Slide 8
Microcontroller
Bluetooth
module
Servo Motor
Driver
Android
phone
E1
E2
Servo
Servo
Servo
Servo
Servo
Servo
Servo
Figure. Overall System Block Diagram

## Slide 9
Application Areas
CNC applications
Industrial manufactures
Drawing applications
Chemical Laboratory

## Slide 10: Android Program
Android Studio SDK
Android Studio Project
Android Application

## Slide 11
1. Android Studio SDK
Android Studio is the official integrated development environment for Google’s Android operating system
Figure . Android Studio Software

## Slide 12
Android Studio Project
Project Tree
Main Activity
UI Design
Permission

## Slide 13
Project Tree
Figure. Project Tree of Robotic Arm Controller
Build for project’s settings
Program folder
Resource folder

## Slide 14
Main Activity
Java programs
Figure. Android Programs in Main Activity.java

## Slide 15
UI Design
Figure. UI Designer of Android Studio
Layout Properties
UI Design of Android App.

## Slide 16
Permission
Figure. Permission Script in Manifest.xml
Permission request
Target SDK

## Slide 17
Android Application
Main User Interface
Menu User Interface
Devices User Interface
Configuration User Interface
Control of Robotic Arm

## Slide 18
Main User Interface
Figure. Main User Interface
Degrees for each Joint
X-Y Joint Sticks
Send Desired degrees

## Slide 19
Devices User Interface
Robotic Arm Devices
To Pair and Scan devices
Figure. Choose Device Dialog

## Slide 20
Menu User Interface
Open the Devices dialog
Exist from app...
Open the app. settings
Figure. Menu Option of Robotic Arm Controller

## Slide 21
Configuration User Interface
Figure. Settings Dialog
For app protection
Lengths of Robotic Arm
Data Store Path
Save the settings

## Slide 22
Control of Robotic Arm
Figure. Controlling the Robotic Arm
Bluetooth Module
Arduino Uno Board
Servo PWM pins
Bluetooth Devices
Servo Degrees

## Slide 23: Implementation Program
Evaluate the mathematical coordinates.
Design the frames according to calculated math.
Design the circuit diagram suitable for servo motor driven.
Write Arduino program and the android application for arm control and to perform desired tasks.

## Slide 24
Expected outcomes
The expected outcomes of the control system of Robotic Arm are:
Getting more stable system and more specific dimension.
May be affected by durable vibration.
May be able to work easily by means of connected android phone.
Saving cost.

## Slide 25
Conclusion
The design is simple enough to incorporate subsequent degrees of freedom, since their is just one grooved shaft to be moved in other planes.
The arm is lighter in weight and occupies lesser floor area to accomplish a given task.

## Slide 27
TECHNOLOGY UNIVERSITY(KALAY)
DEPARTMENT OF ELECTRONIC
ENGINEERING
Supervisor – Daw Cho Thet Nwe
Presented by
Mg Kyaw Win Tun ( VI EC- 29 )
Defense 6.10.2018
DESIGN AND IMPLEMENTATION OF
ROBOTIC ARM
(Arduino Software Implementation)

## Slide 28: Arduino Software implementation
Mg Kyaw Win Tun
VI EC - 29

## Slide 29: Arduino Programming
Robotic Arm Driver Program
Arduino Program installation

## Slide 30
Initialization
Figure. Initialization in Robotic Arm Driver Program
Import servo library
Initialize variables for each servo of joint
Initialize byte array

## Slide 31
Configuration
Figure. Configuration in Robotic Arm Driver Program
Set Arduio Serial’s baud-rate
Set control pins for each servo variable

## Slide 32
Main Program
Figure. Driving Scripts in Robotic Arm Driver Program
Check Serial’s states
Read Serial’s incoming data
Drive the servos by the data from the controller

## Slide 33: Arduino Program Installation
Compile: is to check the written program and to change from C++ language to machine
Upload: is to transfer the program from the computer to the Arduino board using USB Cable
Figure. Upload the Program to Arduino Board

## Slide 34
TECHNOLOGY UNIVERSITY(KALAY)
DEPARTMENT OF ELECTRONIC
ENGINEERING
Supervisor – Daw Cho Thet Nwe
Presented by
Ma Zin Mar Nwe ( VI EC- 3 )
Defense 6.10.2018
DESIGN AND IMPLEMENTATION OF
ROBOTIC ARM
(Circuit Implementation)

## Slide 35: Circuit Implementation
Ma Zin Mar Nwe
VI EC - 3

## Slide 36
Figure. System Architecture of Robotic Arm

## Slide 37
Operating voltage: 5V
i/p voltage: 7-12V(recommended)
i/p voltage: 6-20V(limit)
Digital i/o pin: 14 (of which 6 provide PWM output)
Analog i/p pin : 6
DC current per i/o pin : 40mA
DC current per 3.3V pin : 50mA
Figure. Arduino Uno
Arduino Uno

## Slide 38
Power Supply
Input voltage : 8V-40V
Output voltage : 5V
Output current :3A
Figure. 12V to 5V DC-DC Step-Down Power Supply

## Slide 39
SG90 Servo Motor
Weight:9g
Operating voltage:4.8V(5V)
Stall torque : 1.8kg-cm
Operating speed : 0.1sec/60degree
Figure. SG90 Servo Motor

## Slide 40
MG995 Servo Motor
Figure. MG995 Servo Motor
Weight : 55g
Operating voltage : 4.8V to 7.2V
Stall torque : 8.5kg-cm(4.8V),
10kg-cm(6V)
Operating speed : 0.2sec/60˚(4.8V),
0.16sec/60˚(6V)

## Slide 41
MG996R Servo Motor
Weight :55g
Operating voltage : 4.8V to 7.2V
Stall torque : 9.4kg-cm(4.8V),
11kg-cm(6V)
Operating speed :0.17sec/60˚(4.8V), 0.14sec/60˚(6V)
Figure. MG996R Servo Motor

## Slide 42
Figure. Pin Connections of Servo Motor and Arduino Uno
Connect the red wire to the 5V pin on the Arduino.
Connect the yellow wire to the PWM pin on the Arduino.
Connect the brown wire to the GND pin on the Arduino.

## Slide 43
Bluetooth Module
HC-05 Bluetooth module is an easy to use Bluetooth SPP(Serial Port Protocol) module designed for transparent wireless serial connection setup.
Button
Font View
Back View
Figure. HC-05 Bluetooth Module

## Slide 44
Figure. Pin Connections of HC-05 Bluetooth Module and Arduino Uno
Connect RX pin to TX pin of Arduino
Connect TX pin to RX pin of Arduino
Connect 5V pin to Vin pin of Arduino
Connect GND pin to GND pin of Arduino

## Slide 45
Figure. Pin Connections of LED and Arduino Uno
Connect the anode pin of the red LED to the digital pin 13 of the Arduino
Connect the anode pin of the green LED to the digital pin 8 of the Arduino
Connect the anode pin of the green LED to the digital pin 7 of the Arduino

## Slide 46
TECHNOLOGY UNIVERSITY(KALAY)
DEPARTMENT OF ELECTRONIC
ENGINEERING
Supervisor – Daw Cho Thet Nwe
Presented by
Ma Thuzar Myint ( VI EC- 39 )
Defense 6.10.2018
DESIGN AND IMPLEMENTATION OF
ROBOTIC ARM
(Hardware Implementation)

## Slide 47: Hardware Implementation
Ma Thuzar Myint
VI EC-39

## Slide 48
Hardware Implementation
Components
Frame Designs
Kinematics

## Slide 49
Figure. (a) Drawing View of MG995 (b) MG995 Servo Motor
(a)
(b)
Weight : 55g
Dimension :40.7×19.7×42.9mm
Torque :10kg/cm[6V]
Speed :0.16s/60degree[6V]
Voltage : 4.8V-7.2V
Bandwidth : 5µs
Temperature: 0Ċ-55Ċ

## Slide 50
Figure. (a) Drawing View of MG996R (b) MG996R Servo Motor
(a)
(b)
Weight : 55g
Dimension :40.7×19.7×42.9mm
Torque : 11 kg/cm (6 V)
Speed :0.14 s/60º (6 V)
Voltage : 4.8V-7.2V
Bandwidth : 5µs
Temperature: 0Ċ-55Ċ

## Slide 51
(b)
Figure. (a) Drawing View of SG90 (b) SG90 Servo Motor
(a)
Weight : 14.7 g
Torque : 2.5 kg/cm (6 V)
Speed : 0.1 s/60º (6 V)
Voltage : 4.8V-6V
Bandwidth : 5µs
Temperature: 0Ċ-55Ċ

## Slide 52
Small Ball Bearing
Figure. Small Ball Bearing
Inner diameter d :5mm
Outer diameter B :13mm
Reference speed :95000r/min
Limiting speed :60000r/min
Width :5mm
d1 :8.4mm
D :13mm
D2 :12.3mm
r1,r2 min :0.3mm

## Slide 53
Roller Ball Bearing
Weight :0.7kg
d- Bore :55mm
D – Cup outer diameter: 100mm
B – Cone width :21mm
C – Cup width :18mm
T – Bearing width :22.7mm
Figure. Roller Ball Bearing

## Slide 54
Frame Design
Base
Shoulder
Elbow
Gripper Pitch
Gripper Spin
Gripper

## Slide 55
Figure(a)Base Template of Robotic Arm
(b)Shoulder Template of Robotic Arm
(a)
(b)

## Slide 56
Figure. Elbow Template of Robotic Arm

## Slide 57
Figure. Gripper Pitch Templates of Robotic Arm
(a)For Servo Shaft (b)For Small Ball Bearing
53mm
9mm
13mm
7mm
(a)
(b)

## Slide 58
Figure. Gripper Spin Template of Robotic Arm

## Slide 59
Figure. Gripper Template of Robotic Arm

## Slide 60
Kinematic
Forward Kinematic
Inverse Kinematic
Analytic Method
Cosine Law

## Slide 61
Forward Kinematic
The method for determining the orientation and position of the end-effector
The method for determining given the joint angle and link length

## Slide 62
Inverse Kinematic
To solve the given problem
To know the joint angle required

## Slide 63
Analytic Method
Cos =
]
+
Figure. Analytic Method for Solving the Inverse Kinematic

## Slide 64
Cosine Law
Cos (Cosine Law.)
Figure. Cosine Law